## Slide 1: Stove burner detection
Kristin Rondestvedt

## Slide 2: Objective
It is not uncommon to remove a pot or pan from the burner and forget to turn off the stove. My goal for this project was to implement a device that could help detect if this happens, and to alert the user. ​

## Slide 3: Technologies used
Devices
Arduino BLE Sense 33
Temperature sensor on the BLE Sense 33
OV7675 camera
Grove Chainable LED
Tools/Libraries
Arduino IDE
Edge Impulse to train and deploy image classification model
​Libraries:
  Arduino_LPS22HB
  ChainableLED
  Harvard_TinyMLx
  RunningAverage
  Customized EdgeImpulse image classification

## Slide 4: Implementation details
Image Identification
LED Off
Temperature Sensing
Pot on burner
Logic
Pot on burner, waiting to cool
Pot off burner, temp dropped enough
Trained model using images of my pots/pans
Image taken every 2 seconds
Identify either pot or empty burner
Edge Impulse for training
Temperature reading every 2 seconds
Temperatures added to rolling average
>15/20 pot readings = pot on burner
<5/20 pot readings = pot removed
Pot removal followed by 30 temperature checks triggers temperature deviation check.
At this point, deviation of <5 degrees (temp of last visible pot minus avg temp) triggers an alert.
Alert!

## Slide 5: Challenges
Training
Determining how to identify when there is not a pot – started by training on just things that weren’t a pot. Instead trained on just empty burner.
Difficulty finding image set, so limited training to my own data.
Lighting issues – reflective surface caused false positives.
Sensors
Problems with standalone temperature sensor due to possible library issues. Used BLE Sense’s built-in temperature sensor instead.
Mismatch in camera library that I was using vs. camera library in Edge Impulse deployment.
Logic
Determining how long to wait before checking temp, and how long is sufficient to wait for temp drop. Lots of trial and error.

## Slide 6: future considerations
Internet connectivity to alert via email or text
4-digit display showing temp
Improved pot detection (expand to detect variety of pots/pans)
Improved burner detection for different stove tops. Maybe detect heating element turning red.
Handle more cases
  Monitor room temp before burner turns on.
  If burner on low and didn’t heat up much, check for smaller drop in temp.